## Slide 1
Implement Online Simultaneous Localization And Mapping (SLAM)
with Lidar Scans in MATLAB
Professors: J. Cacace & F. Ruggiero
Student: Arash Hashemi (P44000038)

## Slide 2
1/18
Background Knowledge
What has been done?
Implementation in MATLAB
Results
Outline

## Slide 3
2/18
Background Knowledge
Localization: Estimating the position of the robot
Mapping: Draw a map representing the environment
Environment’s map could help finding the position.
Position could help to map the environment.
SLAM: Simultaneous Localization and mapping can improve
our estimates of positioning and mapping.

## Slide 4
3/18
Background Knowledge
SLAM algorithms are of two types:
online:
Real-time SLAM using filtering techniques such as Kalman Filter and Particle Filter. Continuously building and updating the map.
Offline:
Full SLAM to map the environment using a batch of data (Several consecutive measurements) using smoothing techniques.

## Slide 5
4/18
Background Knowledge
How to measure Position:
Odometry-based:
Using wheel encoders
Velocity-based:
Using IMU
How to observe the environment:
Lidar:
Estimates the distance of an object from sensor

## Slide 6
5/18
Background Knowledge
What is Pose Graph?
A graph made by nodes (Estimated position), edges (Trajectory between two position, or constraint), and the environment
What is Pose Graph Optimization?
Compensation for errors in mapping and positioning when observing a previously visited environment using closure loop
Closure loop:
If two observations are the same or similar, the algorithm consider them the same region and marks a closed loop

## Slide 7
6/18
Background Knowledge
Pose Graph Optimization (Source: https://www.youtube.com/watch?v=saVZtgPyyJQ)
Several Observations
Similar Observation
In two different positions
Real map

## Slide 8
7/18
Background Knowledge
Pose Graph Optimization (Source: https://www.youtube.com/watch?v=saVZtgPyyJQ)

## Slide 9
8/18
What has been done?
Implement online SLAM using lidar scans
Robot’s
Trajectory
Simulink® 3D
Animation™
Lidar
SLAM
Robot’s Positions
Map (+Occupancy grid map)

## Slide 10
9/18
Implementation in MATLAB
Some changes in the example code:
Using own robot trajectory to have a more complex path
Visualization of more loop closure
Showing all steps that a loop closure is present
The aim of the code:
Visualizing the motion of the robot
Performing SLAM
Visualizing the mapping and optimization in steps
Obtaining occupancy grid map

## Slide 11
10/18
Implementation in MATLAB
Importing, declaring, and modifying the trajectory, environment, and objects
Virtual reality world
Objects defining
Objects modification

## Slide 12
11/18
Implementation in MATLAB
Virtual code window

## Slide 13
12/18
Implementation in MATLAB
Defining the SLAM object and its setup
Maximum Lidar Range is 10 meter by default. Due to the noise in long distance observations, it is set to 8 meter
Resolution, threshold and radius of loop closure can change the resulting map.

## Slide 14
13/18
Implementation in MATLAB
Performing loop
Robot Motion and Lidar scan
Mapping visualization
Loop Closure visualization
Optimization visualization
Verifying scan data

## Slide 15
14/18
Implementation in MATLAB
Showing results
Printing all steps that there is a loop closure
Plotting the resulting pose and map

## Slide 16
15/18
Implementation in MATLAB
Occupancy grid map
Occupancy grid map is to set binary values for free and occupied cells, and 0.5 for unknowns.

## Slide 17
16/18
Results
Performing and Optimization

## Slide 18
17/18
Results
Steps and true positions with closure loop

## Slide 19
18/18
Results
Occupancy grid map

## Slide 20
Thanks for your attention